## Slide 1: AME20216 - Lab I L12 – Transient Signals

## Slide 2
Sampling Frequency and Nyquist Criterion
Quality of a digital signal depends on the Sampling Frequency fS
Discrete Digital
“Continuous” Analog
Nyquist Criterion – The maximum frequency component that can be resolved is half the sampling frequency

## Slide 3
Sampling Frequency
Engineering Trade-off:
Large fs
high quality data
large data files
Small fs
low quality data
small data files

## Slide 4
A10 - Thermocouple
Fig. 4.18
Two different metals form a junction – Seebeck or Thermoelectric effect
Thermocouple “type” refers to what metals it uses (Type K, Type J, etc.)
1% accuracy over a wide a temperature range!
Omega.com
IC chip to amplify and linearize the output such that V = (10 mV/C)*T

## Slide 5
A10 - 1st Order Response
Thermocouple (TC)
“1st order response”
Response to an “impulse”

## Slide 6
A10 - Piezoelectric Pressure Transducer
Kulite Sensors - DC
Piezoelectric crystals produce a voltage when deformed
Pressure
Ultrasound - AC
+
+
+
+
-
-
-
-
voltage

## Slide 7
A10 - Piezoelectric Pressure Transducer
Function generator
Oscilloscope
Piezo
Transmitter
Piezo
Receiver
Acoustic
waves

## Slide 8
A10 - 2nd Order Response
ω/ω0
Damping ratio
ζ < 1 underdamped
ζ = 1 critically damped
ζ > 1 overdamped
2 important parameters: resonance frequency ω0 and damping ratio ζ
Driven response, amplitude vs. freq.