## Slide 1: AME20216 - Lab I L11 - Digital Electronics

## Slide 2
Moving Forward
Transient Signals – Measuring and analyzing a signal vs. time (A9 and A10)
Probability and Statistics – Analyzing data and complex systems (HW4)

## Slide 3
Diodes
A diode is a semiconductor device that only allows current to flow in one direction.
Rectification

## Slide 4
Transistors
Used for Amplifiers and Logic Circuits
www.en.wikichip.org
MOSFET
BJT

## Slide 5
Vacuum Tube Amplifiers

## Slide 6
Electronic Numerical Integrator And Computer (ENIAC)
Built by the US Army in 1946.
17,468 vacuum tubes!
https://en.wikipedia.org/wiki/ENIAC
Computer programs used to actually contain bugs!

## Slide 7
Integrated Circuits (I.C.s)
Solid state transistors can be fabricated en masse on a silicon substrate!
https://en.wikipedia.org/wiki/MOSFET

## Slide 8
Integrated Circuits (I.C.s)

## Slide 9
Analog vs. Digital
Analog – A single number is represented by a single voltage.
Digital – A single number is represented by many voltages that form a “binary code”

## Slide 10
Digital Computers
Digital computers – numbers are represented by several voltages in “binary code”
 | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
bit | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1
voltage | 0V | 0V | 3V | 3V | 0V | 0V | 3V | 3V
51 in 8-bit binary code is 00110011
Double precision floating-point variable – 64 bits or 8 bytes
Single precision floating-point variable – 32 bits or 4 bytes
https://en.wikipedia.org/

## Slide 11
Analog-to-Digital Converter
A/D – analog to digital converter (i.e. LabQuest)
Continuous Analog
Discrete Digital
https://nutaq.com
Discrete Digital
D/A – digital to analog converter (i.e. an iPod)
“Continuous” Analog

## Slide 12
MEMS Accelerometers
Micro-Electro-Mechanical Systems (MEMS)
Acceleration causes mass to push on spring and displace the “interdigitated” electrodes,
changes electric capacitance.

## Slide 13
Accelerometers
Boeing 777 glass cockpit.

## Slide 14
ADXL337 – MEMS Accelerometer
3-axis Accelerometer. Analog sensor outputs voltage linearly related to acceleration.
-3g (-30 m/s2) ---> 0V
+3g (+30 m/s2) ---> 3V
output voltage
acceleration

## Slide 15
SparkFun Data Logger
10-bit Analog-to-digital converter (A/D). Saves voltages to a MicroSD card.
0V ---> 0
3V ---> 1023
analog
voltage
10-bit
digital

## Slide 16
2-point Calibration
2-point calibrations of the system are performed by rotating the sensor about its axes.
ay = +1g (9.8 m/s2)
ay = -1g (-9.8 m/s2)

## Slide 17
Telemetry of an RC Car
Acceleration data will be recorded at a sampling frequency fs = 50 Hz.
Important: See “Data Processing” section of A9 lab handout.