## Slide 1: AME20216 - Lab I L4 - Electronics

## Slide 2
Transducers
Omega.com
Manometer
Rotameter
http://www.dwyer-inst.com

## Slide 3
A3 – Electronics I
Solderless breadboard

## Slide 4
Internet of Things (IoT) – Sensors galore!

## Slide 5
Electricity: Review of Physics II
Charge: q [Coulombs]
+
-
Current: [C/s] = [Amperes]
Voltage: V “electrostatic potential energy”
[Joules/Coulomb] = [Volts]

## Slide 6
Ohm’s Law
Resistance: R [Ohms] = [Ω]
Resistors in Parallel
Resistors in Series
R1
R2
R1
R2

## Slide 7
Joule Heating
Electrons collide with metal atoms, transfer kinetic energy.
Metal heats up.
Power Dissipated:
[Joules/second] = [Watts] = [W]
Always valid
Only valid for
“Ohmic” devices

## Slide 8
Digital Multimeter (DMM)
Can measure current, voltage, and resistance.

## Slide 9
Digital Multimeters
Extech Handheld DMM
Keysight Precision DMM
Can measure current, voltage, and resistance.

## Slide 10
Kirchhoff’s Circuit Laws
1. Current Law: Current IN = Current OUT
2. Voltage Law: sum of voltages around a closed loop is Zero

## Slide 11
“Floating” voltage divider circuit
“Grounded” voltage divider circuit
Assume the ground is always at zero volts.

## Slide 12
Voltage Divider

## Slide 13
Cadmium Sulfide (CdS) Photocell
Resistance of Photocell changes when illuminated.