## Slide 1: AME20216 - Lab I L8 – Solar Energy

## Slide 2
Kleiber’s Law: Metabolism vs. Mass
http://eesc.columbia.edu/courses/ees/life/lectures/lect03.html

## Slide 3
Energy Consumption
Human metabolism ~ 100W
Human “social metabolism” ~ 10,000W

## Slide 4
Energy Consumption
https://en.wikipedia.org/wiki/Human_overpopulation#/media/File:Population_curve.svg
Population over 7 billion and growing!

## Slide 5
Energy Consumption
Energy Input
Economy
3x1012 W (3 TW)
~10,000W per person!
Work Output
GDP and $$$
1x1012 W
~34% used
Entropy
Output
Waste heat:
2x1012 W
~66% wasted

## Slide 6
A6 and A7 - Solar Panels
173 Million GigaWatts of power are incident on planet earth!
10,000 times more than total human consumption.

## Slide 7
A6/A7 – Solar Panels

## Slide 8
What is Light?
Light is an electromagnetic wave that travels at the speed of light.
“Visible Light” has a wavelength in the 400 – 700nm range.
Wavelength determines color.

## Slide 9
Non-ideal Power Supply
Solar panel is a non-ideal power supply
Voltage “Droop”

## Slide 10
Non-ideal Power Supply
Power output depends on load resistance RL
qL
RL
Max power occurs when
RL = RS
“Impedance matching”