## Slide 1
Semiconductor Devices
Diodes and LEDs
Transistors
Solar Panels

## Slide 2
Diodes
A diode is a semiconductor device that only allows current to flow in one direction.
Rectification

## Slide 3
Transistors
Used for Amplifiers and Logic Circuits
www.en.wikichip.org
MOSFET
BJT

## Slide 4
Vacuum Tube Amplifiers

## Slide 5
Electronic Numerical Integrator And Computer (ENIAC)
Built by the US Army in 1946.
17,468 vacuum tubes!
https://en.wikipedia.org/wiki/ENIAC
Computer programs used to actually contain bugs!

## Slide 6
Integrated Circuits (I.C.s)
Solid state transistors can be fabricated en masse on a silicon substrate!
https://en.wikipedia.org/wiki/MOSFET

## Slide 7
Integrated Circuits (I.C.s)

## Slide 8
Op-Amp Integrated Circuit

## Slide 9
Amplifiers
Used to increase the signal-to-noise-ratio (SNR).
“Gain”
Differential Amplifier cancels out the “common” noise, only amplifies signal.
“The numbers all go to eleven.”

## Slide 10
Op-Amps and Analog Computers
Analog computers – a number is represented as a single voltage
Differentiator
Integrator
Summing amplifier
http://www.electronics-tutorials.ws/opamp/opamp_4.html
https://en.wikipedia.org

## Slide 11
Digital Logic Circuits – 2 bit adder

## Slide 12
Analog vs. Digital
Analog computer – A single number is represented by a single voltage.
Integrator
Differentiator
Digital computer – A single number is represented by many voltages that form a “binary code”

## Slide 13
Digital Computers
FLOPS – Float Point Operations Per Second
Nintendo 64 ~ 108 FLOPS
PS3, Samsung Galaxy S5 ~ 1011 FLOPS
IBM Summit supercomputer ~ 1017 FLOPS

## Slide 14
MEMS Accelerometers
3-axis gyro from an iPhone 4
Micro-Electro-Mechanical Systems (MEMS)
Acceleration causes mass to push on spring and displace the “interdigitated” electrodes,
changes electric capacitance.

## Slide 15
Accelerometers
Boeing 777 glass cockpit.

## Slide 16
ADXL337 – MEMS Accelerometer
3-axis Accelerometer. Analog sensor outputs voltage linearly related to acceleration.
-3g (-30 m/s2) ---> 0V
+3g (+30 m/s2) ---> 3V
output voltage
acceleration

## Slide 17
SparkFun Data Logger
10-bit Analog-to-digital converter (A/D). Saves voltages to a MicroSD card.
0V ---> 0
3V ---> 1023
analog
voltage
10-bit
digital

## Slide 18
2-point Calibration
2-point calibrations of the system are performed by rotating the sensor about its axes.
ay = +1g (9.8 m/s2)
ay = -1g (-9.8 m/s2)

## Slide 19
Telemetry of an RC Car
Acceleration data will be recorded at a sampling frequency fs = 50 Hz.
Important: See “Data Processing” section of A9 lab handout.