## Slide 1
Sensor
Chapter 6 and more!

## Slide 2
Manometer
Measures pressure

## Slide 3
Sensitivity
Inclined Manometer
More sensitive
Less range
http://www.dwyer-inst.com
U-tube Manometer
Less sensitive
Greater range

## Slide 4
Capacitive Pressure Transducer
Pressure pushes capacitor plates closer together
Capacitance-to-voltage IC chip
Capacitive presssure sensor
VOUT
COUT

## Slide 5
Strain Gauge (or Gage)
Fig. 4.4
Measures strain based on change in resistance
Ge ≈ 2 “gage factor”
Often wired up in a Wheatsone bridge configurartion

## Slide 6
Thermistor
Works the same as an RTD, except the sensing material is made of a ceramic or a semiconductor.
Steinhart Eq.
Non-linear response

## Slide 7
RTD – Resistance Temperature Detector
The resistivity of a metal changes linearly with temperature.

## Slide 8
Thermocouple
Fig. 4.18
Uses the thermoelectric effect to convert temperature to voltage.
Two different metals form a junction – Seebeck effect
Thermocouple “type” refers to what metals it uses (Type K, Type J, etc.)
1% accuracy over a wide a temperature range!
Omega.com
IC chip to amplify and linearize the output such that V = (10 mV/C)*T

## Slide 9
Black Body Radiation
Warm objects emit “black body radiation”.
Omega.com
T~300K Infrared
T~1000K Red
>5000K “White hot”

## Slide 10
Pyrometer
Determines temperature from infrared blackbody radiation
Useful for non-contact, high-temeprature measurements
Omega.com

## Slide 11
Temperature Measurements
RTD or Thermistor: 200 – 500K
Thermocouple: 200 – 1000K
  Different “types” have different ranges
Pyrometer: T > 750K – “non-contact”
Omega.com
Omega.com

## Slide 12
Pitot Static Probe
Measures fluid velocity u using Bernoulli’s law

## Slide 13
Rotameter
Measures flow rate.
Viscous drag causes a bead to levitate at a certain height.
Omega.com

## Slide 14
Venturi Tube
Some times called a “variable area flow meter”.
Uses Bernoulli’s law to measure flow rate Q = volume/sec.

## Slide 15
Hotwire Anemometer
Measures fluid velocity based on the convective cooling of a thin, heated wire.
Wire serves as both a resistive heater and as an RTD.

## Slide 16
Schlieren Visualization
Schlieren video: https://www.youtube.com/watch?v=JhlEkEk7igs (11:10)
Optical system is highly sensitive to changes in gas density, often used to visualize shock waves in an hypersonic flow.
Fig. 4.17

## Slide 17
Particle Image Velocimetry
Flow Visualization:
https://www.youtube.com/watch?v=nuQyKGuXJOs&index=5&list=PL0EC6527BE871ABA3 (11:00)
532 nm green Nd:YAG laser
used as a flash bulb
https://web.engr.oregonstate.edu
Compares two successive images of “seed particles”

## Slide 18
Particle Image Velocimetry
NACA Video: H2 Bubbles (11:00)
http://research.ae.utexas.edu
Fog machines work surprisingly well at creating seed particles in gas. Very small glass beads are often used in liquids.

## Slide 19
Ultrasonic Range Finder
Emits an ultrasonic pulse, waits for the echo
Δt
Uses the speed of sound to calculate distance

## Slide 20
LIDAR
Light Detection And Ranging
Laser emits light, back-scatter or reflection recorded. Uses the speed of light to calculate distance.

## Slide 21
Global Positioning System
An array of 24+ satellites broadcast their current location and timestamp.
The speed of light is used to calculate distance from each satellite
GPS receivers listen for signals from satellites.
Trilateration is used to calculate the position of the receiver.

## Slide 22
Semiconductor Devices
Diodes and LEDs
Transistors – Used for amplifiers and logic circuits

## Slide 23
Integrated Circuits (I.C.s)
Wafers are diced up and packaged as IC chips.
DIP – “Dual inline package”

## Slide 24
Cadmium Sulfide (CdS) Photocell
Resistance of Photocell changes when illuminated.

## Slide 25
Orientation
Mechanical parts can rotate to various angles.
Robot football

## Slide 26
Tachometers
Measures angular frequency ω or RPMs.
Some work based on magnetic inductance.
Others work optically
(i.e. Lab 1 PS3 fan speed)
Old fashioned ones are mechanical

## Slide 27
Orientation
Potentiometers convert angle into a resistance.
Works like a voltage divider!

## Slide 28
Quadrature Encoders
A Quadrature encoder counts electrical pulses as slotted wheel passes through a photocell.
Measures angular position and speed.

## Slide 29
Attitude (Orientation)
Aircraft can rotate about 3-principle axes.

## Slide 30
Gyroscopes
Attitude can be measured using a gyroscope.
Conservation of angular momentum causes flywheel to maintain its orientation.

## Slide 31
Modern Accelerometers
“interdigitated” electrodes
3-axis gyro from an iPhone 4
Micro-Electro-Mechanical Systems (MEMS) have largely replace gyroscopes for intertial measurements.

## Slide 32
Attitude Heading Reference System (AHRS)
Complete suite of accelerometers and gyroscopes for digital avionic systems.

## Slide 33
Avionics

## Slide 34
Vendors and Manufacturers
Basic electronic components – Jameco, Digikey, and Mouser
Omega Engineering Manufactures and sells many different temperature, pressure, and flow sensors
Honeywell
Manufactures and sells a variety of sensors commonly used in AME industry